## Slide 1: Networks
Network-based design.
  Communication analysis.
  System performance analysis.
Internet-enabled systems.

## Slide 2: Communication analysis
First, understand delay for single message.
Delay for multiple messages depends on:
  network protocol;
  devices on network.

## Slide 3: Message delay
Assume:
  single message;
  no contention.
Delay:
  tm = tx + tn + tr
  = xmtr overhead + network xmit time + rcvr overhead

## Slide 4: Example: I2C message delay
Network transmission time dominates.
Assume 100 kbits/sec, one 8-bit byte.
Number of bits in packet:
  npacket = start + address + data + stop
  = 1 + 8 + 8 + 1 = 18 bits
Time required to transmit: 1.8 x 10-4 sec.
20 instructions on 8 MHz controller adds 2.5 x 10-6 delay on xmtr, rcvr.

## Slide 5: Multiple messages
If messages can interfere with each other, analysis is more complex.
Model total message delay:
  ty = td + tm
  = wait time for network + message delay

## Slide 6: Arbitration and delay
Fixed-priority arbitration introduces unbounded delay for all but highest-priority device.
  Unless higher-priority devices are known to have limited rates that allow lower devices to transmit.
Round-robin arbitration introduces bounded delay proportional to N.

## Slide 7: Example: adjusting messages to reduce delay
Task graph:
Network:
P1
P2
P3
d1
d2
M1
M2
M3
allocation
3
4
3
execution time
Transmission time = 4

## Slide 8: Initial schedule
time
M1
M2
M3
network
0
20
10
5
15
P1
P2
d1
d1
P3
Time = 15

## Slide 9: New design
Modify P3:
  reads one packet of d1, one packet of d2
  computes partial result
  continues to next packet

## Slide 10: New schedule
time
M1
M2
M3
network
0
20
10
5
15
P1
P2
d1
P3
d2
d1
P3
d2
d1
P3
d2
d1
P3
d2
Time = 12

## Slide 11: Further complications
Acknowledgment time.
Transmission errors.

## Slide 12: Priority inversion in networks
In many networks, a packet cannot be interrupted.
Result is priority inversion:
  low-priority message holds up higher-priority message.
Doesn’t cause deadlock, but can slow down important communications.

## Slide 13: Multihop networks
In multihop networks, one node receives message, then retransmits to destination (or intermediate).
A
B
C
hop 1
hop 2
Network 1
Network 2

## Slide 14: System performance analysis
System analysis is difficult in general.
  multiprocessor performance analysis is hard;
  communication performance analysis is hard.
Simple example: uncertainty in P1 finish time -> uncertainty in P2 start time.
P1
P2

## Slide 15: Analysis challenges
P2 and P3 can delay each other, even though they are in separate tasks.
Delays in P1 propagate to P2, then P3, then to P4.
P2
P3
P1
P4

## Slide 16: Lower bounds on system
Computational requirements:
  sum up process requirements over least-common multiple of periods, average over one period.
Communication requirements:
  Count all transmissions in one period.

## Slide 17: Hardware platform design
Need to choose:
  number and types of PEs;
  number and types of networks.
Evaluate a platform by allocating processes, scheduling processes and communication.

## Slide 18: I/O-intensive systems
Start with I/O devices, then consider computation:
  inventory required devices;
  identify critical deadlines;
  chooses devices that can share PEs;
  analyze communication times;
  choose PEs to go with devices.

## Slide 19: Computation-intensive systems
Start with shortest-deadline tasks:
  Put shortest-deadline tasks on separate PEs.
  Check for interference on critical communications.
  Allocate low-priority tasks to common PEs wherever possible.
Balance loads wherever possible.

## Slide 20: Internet-enabled embedded system
Internet-enabled embedded system: any embedded system that includes an Internet interface (e.g., refrigerator).
Internet appliance: embedded system designed for a particular Internet task (e.g. email).

## Slide 21: Examples
Laser printer.
Personal digital assistant (PDA).
Home automation system.

## Slide 22: Example: Javacam
Hardware platform:
  parallel-port camera;
  National Semi NS486SXF;
  1.5 Mbytes memory.
Uses memory-efficient Java Nanokernel.

## Slide 23: Javacam architecture
Web browser
QuickCam
486
Java nanokernel
Java VM
HTTP
Quickcam
server
QuickCam
applet