## Slide 1: CPUs
CPU performance
CPU power consumption.

## Slide 2: Elements of CPU performance
Cycle time.
CPU pipeline.
Memory system.

## Slide 3: Pipelining
Several instructions are executed simultaneously at different stages of completion.
Various conditions can cause pipeline bubbles that reduce utilization:
  branches;
  memory system delays;
  etc.

## Slide 4: Pipeline structures
Both ARM and SHARC have 3-stage pipes:
  fetch instruction from memory;
  decode opcode and operands;
  execute.

## Slide 5: ARM pipeline execution
add r0,r1,#5
sub r2,r3,r6
cmp r2,#3
fetch
time
decode
fetch
execute
decode
fetch
execute
decode
execute
1
2
3

## Slide 6: Performance measures
Latency: time it takes for an instruction to get through the pipeline.
Throughput: number of instructions executed per time period.
Pipelining increases throughput without reducing latency.

## Slide 7: Pipeline stalls
If every step cannot be completed in the same amount of time, pipeline stalls.
Bubbles introduced by stall increase latency, reduce throughput.

## Slide 8: ARM multi-cycle LDMIA instruction
fetch
decode
ex ld r2
ldmia
r0,{r2,r3}
sub
r2,r3,r6
cmp
r2,#3
ex ld r3
fetch
time
decode
ex sub
fetch
decode
ex cmp

## Slide 9: Control stalls
Branches often introduce stalls (branch penalty).
  Stall time may depend on whether branch is taken.
May have to squash instructions that already started executing.
Don’t know what to fetch until condition is evaluated.

## Slide 10: ARM pipelined branch
time
fetch
decode
ex bne
bne foo
sub
r2,r3,r6
fetch
decode
foo add
r0,r1,r2
ex bne
fetch
decode
ex add
ex bne

## Slide 11: Delayed branch
To increase pipeline efficiency, delayed branch mechanism requires n instructions after branch always executed whether branch is executed or not.
SHARC supports delayed and non-delayed branches.
  Specified by bit in branch instruction.
  2 instruction branch delay slot.

## Slide 12: Example: SHARC code scheduling
L1=5;
DM(I0,M1)=R1;
L8=8;
DM(I8,M9)=R2;
CPU cannot use DAG on cycle just after loading DAG’s register.
  CPU performs NOP between register assign and DM.

## Slide 13: Rescheduled SHARC code
L1=5;
L8=8;
DM(I0,M1)=R1;
DM(I8,M9)=R2;
Avoids two NOP cycles.

## Slide 14: Example: ARM execution time
Determine execution time of FIR filter:
  for (i=0; i<N; i++)
  f = f + c[i]*x[i];
Only branch in loop test may take more than one cycle.
  BLT loop takes 1 cycle best case, 3 worst case.

## Slide 15: Superscalar execution
Superscalar processor can execute several instructions per cycle.
  Uses multiple pipelined data paths.
Programs execute faster, but it is harder to determine how much faster.

## Slide 16: Data dependencies
Execution time depends on operands, not just opcode.
Superscalar CPU checks data dependencies dynamically:
add r2,r0,r1
add r3,r2,r5
data dependency
r0
r1
r2
r5
r3

## Slide 17: Memory system performance
Caches introduce indeterminacy in execution time.
  Depends on order of execution.
Cache miss penalty: added time due to a cache miss.
Several reasons for a miss: compulsory, conflict, capacity.

## Slide 18: CPU power consumption
Most modern CPUs are designed with power consumption in mind to some degree.
Power vs. energy:
  heat depends on power consumption;
  battery life depends on energy consumption.

## Slide 19: CMOS power consumption
Voltage drops: power consumption proportional to V2.
Toggling: more activity means more power.
Leakage: basic circuit characteristics; can be eliminated by disconnecting power.

## Slide 20: CPU power-saving strategies
Reduce power supply voltage.
Run at lower clock frequency.
Disable function units with control signals when not in use.
Disconnect parts from power supply when not in use.

## Slide 21: Power management styles
Static power management: does not depend on CPU activity.
  Example: user-activated power-down mode.
Dynamic power management: based on CPU activity.
  Example: disabling off function units.

## Slide 22: Application: PowerPC 603 energy features
Provides doze, nap, sleep modes.
Dynamic power management features:
  Uses static logic.
  Can shut down unused execution units.
  Cache organized into subarrays to minimize amount of active circuitry.

## Slide 23: PowerPC 603 activity
Percentage of time units are idle for SPEC integer/floating-point:
unit Specint92 Specfp92
D cache 29% 28%
I cache 29% 17%
load/store 35% 17%
fixed-point 38% 76%
floating-point 99% 30%
system register 89% 97%

## Slide 24: Power-down costs
Going into a power-down mode costs:
  time;
  energy.
Must determine if going into mode is worthwhile.
Can model CPU power states with power state machine.

## Slide 25: Application: StrongARM SA-1100 power saving
Processor takes two supplies:
  VDD is main 3.3V supply.
  VDDX is 1.5V.
Three power modes:
  Run: normal operation.
  Idle: stops CPU clock, with logic still powered.
  Sleep: shuts off most of chip activity; 3 steps, each about 30 s; wakeup takes > 10 ms.

## Slide 26: SA-1100 power state machine
run
idle
sleep
Prun = 400 mW
Pidle = 50 mW
Psleep = 0.16 mW
10 s
10 s
90 s
160 ms
90 s