## Slide 1: Networking for Embedded Systems
Why we use networks.
Network abstractions.
Example networks.

## Slide 2: Network elements
PE
PE
PE
network
communication link
distributed computing platform:
PEs may be CPUs or ASICs.

## Slide 3: Networks in embedded systems
PE
PE
sensor
PE
actuator
initial processing
more processing

## Slide 4: Why distributed?
Higher performance at lower cost.
Physically distributed activities---time constants may not allow transmission to central site.
Improved debugging---use one CPU in network to debug others.
May buy subsystems that have embedded processors.

## Slide 5: Network abstractions
International Standards Organization (ISO) developed the Open Systems Interconnection (OSI) model to describe networks:
  7-layer model.
Provides a standard way to classify network components and operations.

## Slide 6: OSI model
physical
mechanical, electrical
data link
reliable data transport
network
end-to-end service
transport
connections
presentation
data format
session
application dialog control
application
end-use interface

## Slide 7: OSI layers
Physical: connectors, bit formats, etc.
Data link: error detection and control across a single link (single hop).
Network: end-to-end multi-hop data communication.
Transport: provides connections; may optimize network resources.

## Slide 8: OSI layers, cont’d.
Session: services for end-user applications: data grouping, checkpointing, etc.
Presentation: data formats, transformation services.
Application: interface between network and end-user programs.

## Slide 9: Hardware architectures
Many different types of networks:
  topology;
  scheduling of communication;
  routing.

## Slide 10: Point-to-point networks
One source, one or more destinations, no data switching (serial port):
PE 1
PE 2
PE 3
link 1
link 2

## Slide 11: Bus networks
Common physical connection:
PE 1
PE 2
PE 3
PE 4
header
address
data
ECC
packet format

## Slide 12: Bus arbitration
Fixed: Same order of resolution every time.
Fair: every PE has same access over long periods.
  round-robin: rotate top priority among Pes.
A,B,C
A,B,C
fixed
round-robin
A
B
C
A
B
C
A
B
C
A
B
C

## Slide 13: Crossbar
in1
in2
in3
in4
out1
out2
out3
out4

## Slide 14: Crossbar characteristics
Non-blocking.
Can handle arbitrary multi-cast combinations.
Size proportional to n2.

## Slide 15: Multi-stage networks
Use several stages of switching elements.
Often blocking.
Often smaller than crossbar.

## Slide 16: Message-based programming
Transport layer provides message-based programming interface:
  send_msg(adrs,data1);
Data must be broken into packets at source, reassembled at destination.
Data-push programming: make things happen in network based on data transfers.

## Slide 17: I2C bus
Designed for low-cost, medium data rate applications.
Characteristics:
  serial;
  multiple-master;
  fixed-priority arbitration.
Several microcontrollers come with built-in I2C controllers.

## Slide 18: I2C physical layer
master 1
master 1
slave 1
slave 1
SCL
SDL
data line
clock line

## Slide 19: I2C data format
SCL
SDL
...
MSB
start
...
ack
...

## Slide 20: I2C electrical interface
SDL
+
Open collector interface:
SCL
+

## Slide 21: I2C signaling
Sender pulls down bus for 0.
Sender listens to bus---if it tried to send a 1 and heard a 0, someone else is simultaneously transmitting.
Transmissions occur in 8-bit bytes.

## Slide 22: I2C data link layer
Every device has an address (7 bits in standard, 10 bits in extension).
  Bit 8 of address signals read or write.
General call address allows broadcast.

## Slide 23: I2C bus arbitration
Sender listens while sending address.
When sender hears a conflict, if its address is higher, it stops signaling.
Low-priority senders relinquish control early enough in clock cycle to allow bit to be transmitted reliably.

## Slide 24: I2C transmissions
multi-byte write
read from slave
write, then read
S
adrs
0
data
data
P
S
adrs
1
data
P
S
adrs
0
data
S
adrs
1
data
P

## Slide 25: Multiprocessor networks
Multiple DSPs are often connected by high-speed networks for signal processing:
DSP
DSP
DSP
DSP

## Slide 26: SHARC link ports
Six per CPU.
Four bits per link port.
Packets have 32- or 48-bit payload.
Can be controlled by DMA.
Are half-duplex---must be turned around by program.

## Slide 27: Ethernet
Dominant non-telephone LAN.
Versions: 10 Mb/s, 100 Mb/s, 1 Gb/s
Goal: reliable communication over an unreliable medium.

## Slide 28: Ethernet topology
Bus-based system, several possible physical layers:
A
B
C

## Slide 29: CSMA/CD
Carrier sense multiple access with collision detection:
  sense collisions;
  exponentially back off in time;
  retransmit.

## Slide 30: Exponential back-off times
time

## Slide 31: Ethernet packet format
preamble
start
frame
source
adrs
dest
adrs
data
payload
length
padding
CRC

## Slide 32: Ethernet performance
Quality-of-service tends to non-linearly decrease at high load levels.
Can’t guarantee real-time deadlines. However, may provide very good service at proper load levels.

## Slide 33: Internet Protocol
Internet Protocol (IP) is basis for Internet.
Provides an internetworking standard: between two Ethernets, Ethernet and token ring, etc.
Higher-level services are built on top of IP.

## Slide 34: IP in communication
physical
data link
network
transport
presentation
application
session
physical
data link
network
transport
presentation
application
session
physical
data link
network
node A
router
node B
IP

## Slide 35: IP packet
Includes:
  version, service type, length
  time to live, protocol
  source and destination address
  data payload
Maximum data payload is 65,535 bytes.

## Slide 36: IP addresses
32 bits in early IP, 128 bits in IPv6.
Typically written in form xxx.xx.xx.xx.
Names (foo.baz.com) translated to IP address by domain name server (DNS).

## Slide 37: Internet routing
Best effort routing:
  doesn’t guarantee data delivery at IP layer.
Routing can vary:
  session to session;
  packet to packet.

## Slide 38: Higher-level Internet services
Transmission Control Protocol (TCP) provides connection-oriented service.
Quality-of-service (QoS) guaranteed services are under development.

## Slide 39: The Internet service stack
IP
UDP
SNMP
TCP
User
Datagram
Protocol
FTP
HTTP
SMTP
telnet