## Slide 1: Instruction sets
Computer architecture taxonomy.
Assembly language.

## Slide 2: von Neumann architecture
Memory holds data, instructions.
Central processing unit (CPU) fetches instructions from memory.
  Separate CPU and memory distinguishes programmable computer.
CPU registers help out: program counter (PC), instruction register (IR), general-purpose registers, etc.

## Slide 3: CPU + memory
memory
CPU
PC
address
data
IR
ADD r5,r1,r3
200
200
ADD r5,r1,r3

## Slide 4: Harvard architecture
CPU
PC
data memory
program memory
address
data
address
data

## Slide 5: von Neumann vs. Harvard
Harvard can’t use self-modifying code.
Harvard allows two simultaneous memory fetches.
Most DSPs use Harvard architecture for streaming data:
  greater memory bandwidth;
  more predictable bandwidth.

## Slide 6: RISC vs. CISC
Complex instruction set computer (CISC):
  many addressing modes;
  many operations.
Reduced instruction set computer (RISC):
  load/store;
  pipelinable instructions.

## Slide 7: Instruction set characteristics
Fixed vs. variable length.
Addressing modes.
Number of operands.
Types of operands.

## Slide 8: Programming model
Programming model: registers visible to the programmer.
Some registers are not visible (IR).

## Slide 9: Multiple implementations
Successful architectures have several implementations:
  varying clock speeds;
  different bus widths;
  different cache sizes;
  etc.

## Slide 10: Assembly language
One-to-one with instructions (more or less).
Basic features:
  One instruction per line.
  Labels provide names for addresses (usually in first column).
  Instructions often start in later columns.
  Columns run to end of line.

## Slide 11: ARM assembly language example
label1 ADR r4,c
LDR r0,[r4] ; a comment
ADR r4,d
LDR r1,[r4]
SUB r0,r0,r1 ; comment

## Slide 12: Pseudo-ops
Some assembler directives don’t correspond directly to instructions:
  Define current address.
  Reserve storage.
  Constants.