## Slide 1: CPUs
Input and output.
Supervisor mode, exceptions, traps.
Co-processors.

## Slide 2: I/O devices
Usually includes some non-digital component.
Typical digital interface to CPU:
CPU
status
reg
data
reg
mechanism

## Slide 3: Application: 8251 UART
Universal asynchronous receiver transmitter (UART) : provides serial communication.
8251 functions are integrated into standard PC interface chip.
Allows many communication parameters to be programmed.

## Slide 4: Serial communication
Characters are transmitted separately:
time
bit 0
bit 1
bit n-1
no
char
start
stop
...

## Slide 5: Serial communication parameters
Baud (bit) rate.
Number of bits per character.
Parity/no parity.
Even/odd parity.
Length of stop bit (1, 1.5, 2 bits).

## Slide 6: 8251 CPU interface
CPU
8251
status
(8 bit)
data
(8 bit)
serial
port
xmit/
rcv

## Slide 7: Programming I/O
Two types of instructions can support I/O:
  special-purpose I/O instructions;
  memory-mapped load/store instructions.
Intel x86 provides in, out instructions. Most other CPUs use memory-mapped I/O.
I/O instructions do not preclude memory-mapped I/O.

## Slide 8: ARM memory-mapped I/O
Define location for device:
DEV1 EQU 0x1000
Read/write code:
  LDR r1,#DEV1 ; set up device adrs
  LDR r0,[r1] ; read DEV1
  LDR r0,#8 ; set up value to write
  STR r0,[r1] ; write value to device

## Slide 9: SHARC memory mapped I/O
Device must be in external memory space (above 0x400000).
Use DM to control access:
  I0 = 0x400000;
  M0 = 0;
  R1 = DM(I0,M0);

## Slide 10: Peek and poke
Traditional HLL interfaces:
  int peek(char *location) {
  return *location; }
  void poke(char *location, char newval) {
  (*location) = newval; }

## Slide 11: Busy/wait output
Simplest way to program device.
  Use instructions to test when device is ready.
current_char = mystring;
while (*current_char != ‘\0’) {
poke(OUT_CHAR,*current_char);
while (peek(OUT_STATUS) != 0);
current_char++;
}

## Slide 12: Simultaneous busy/wait input and output
while (TRUE) {
/* read */
while (peek(IN_STATUS) == 0);
achar = (char)peek(IN_DATA);
/* write */
poke(OUT_DATA,achar);
poke(OUT_STATUS,1);
while (peek(OUT_STATUS) != 0);
}

## Slide 13: Interrupt I/O
Busy/wait is very inefficient.
  CPU can’t do other work while testing device.
  Hard to do simultaneous I/O.
Interrupts allow a device to change the flow of control in the CPU.
  Causes subroutine call to handle device.

## Slide 14: Interrupt interface
CPU
status
reg
data
reg
mechanism
PC
intr request
intr ack
data/address
IR

## Slide 15: Interrupt behavior
Based on subroutine call mechanism.
Interrupt forces next instruction to be a subroutine call to a predetermined location.
  Return address is saved to resume executing foreground program.

## Slide 16: Interrupt physical interface
CPU and device are connected by CPU bus.
CPU and device handshake:
  device asserts interrupt request;
  CPU asserts interrupt acknowledge when it can handle the interrupt.

## Slide 17: Example: character I/O handlers
void input_handler() {
achar = peek(IN_DATA);
gotchar = TRUE;
poke(IN_STATUS,0);
}
void output_handler() {
}

## Slide 18: Example: interrupt-driven main program
main() {
while (TRUE) {
if (gotchar) {
poke(OUT_DATA,achar);
poke(OUT_STATUS,1);
gotchar = FALSE;
}
}
}

## Slide 19: Example: interrupt I/O with buffers
Queue for characters:
head
tail
head
tail
a

## Slide 20: Buffer-based input handler
void input_handler() {
char achar;
if (full_buffer()) error = 1;
else { achar = peek(IN_DATA); add_char(achar); }
poke(IN_STATUS,0);
if (nchars == 1)
{ poke(OUT_DATA,remove_char(); poke(OUT_STATUS,1); }
}

## Slide 21: I/O sequence diagram
:foreground
:input
:output
:queue
empty
a
empty
b
bc
c

## Slide 22: Debugging interrupt code
What if you forget to change registers?
  Foreground program can exhibit mysterious bugs.
  Bugs will be hard to repeat---depend on interrupt timing.

## Slide 23: Priorities and vectors
Two mechanisms allow us to make interrupts more specific:
  Priorities determine what interrupt gets CPU first.
  Vectors determine what code is called for each type of interrupt.
Mechanisms are orthogonal: most CPUs provide both.

## Slide 24: Prioritized interrupts
CPU
device 1
device 2
device n
L1 L2 .. Ln
interrupt
acknowledge

## Slide 25: Interrupt prioritization
Masking: interrupt with priority lower than current priority is not recognized until pending interrupt is complete.
Non-maskable interrupt (NMI): highest-priority, never masked.
  Often used for power-down.

## Slide 26: Example: Prioritized I/O
:interrupts
:foreground
:A
:B
:C
B
A,B
C
A

## Slide 27: Interrupt vectors
Allow different devices to be handled by different code.
Interrupt vector table:
handler 0
handler 1
handler 2
handler 3
Interrupt
vector
table head

## Slide 28: Interrupt vector acquisition
:CPU
:device
receive
request
receive
ack
receive
vector

## Slide 29: Generic interrupt mechanism
intr?
N
Y
Assume priority selection is handled before this point.
N
ignore
Y
ack
vector?
Y
Y
N
timeout?
Y
bus error
call table[vector]
intr priority > current priority?
continue
execution

## Slide 30: Interrupt sequence
CPU acknowledges request.
Device sends vector.
CPU calls handler.
Software processes request.
CPU restores state to foreground program.

## Slide 31: Sources of interrupt overhead
Handler execution time.
Interrupt mechanism overhead.
Register save/restore.
Pipeline-related penalties.
Cache-related penalties.

## Slide 32: ARM interrupts
ARM7 supports two types of interrupts:
  Fast interrupt requests (FIQs).
  Interrupt requests (IRQs).
Interrupt table starts at location 0.

## Slide 33: ARM interrupt procedure
CPU actions:
  Save PC. Copy CPSR to SPSR.
  Force bits in CPSR to record interrupt.
  Force PC to vector.
Handler responsibilities:
  Restore proper PC.
  Restore CPSR from SPSR.
  Clear interrupt disable flags.

## Slide 34: ARM interrupt latency
Worst-case latency to respond to interrupt is 27 cycles:
  Two cycles to synchronize external request.
  Up to 20 cycles to complete current instruction.
  Three cycles for data abort.
  Two cycles to enter interrupt handling state.

## Slide 35: SHARC interrupt structure
Interrupts are vectored and prioritized.
Priorities are fixed: reset highest, user SW interrupt 3 lowest.
Vectors are also fixed. Vector is offset in vector table. Table starts at 0x20000 in internal memory, 0x40000 in external memory.v

## Slide 36: SHARC interrupt sequence
Start: must be executing or IDLE/IDLE16.
1. Output appropriate interrupt vector address.
2. Push PC value onto PC stack.
3. Set bit in interrupt latch register.
4. Set IMASKP to current nesting state.

## Slide 37: SHARC interrupt return
Initiated by RTI instruction.
1. Return to address at top of PC stack.
2. Pop PC stack.
3. Pop status stack if appropriate.
4. Clear bits in interrupt latch register and IMASKP.

## Slide 38: SHARC interrupt performance
Three stages of response:
  1 cycle: synchronization and latching;
  1 cycle: recognition;
  2 cycles: brancing to vector.
Total latency: 3 cycles.
Multiprocessor vector interrupts have 6 cycle latency.

## Slide 39: Supervisor mode
May want to provide protective barriers between programs.
  Avoid memory corruption.
Need supervisor mode to manage the various programs.
SHARC does not have a supervisor mode.

## Slide 40: ARM supervisor mode
Use SWI instruction to enter supervisor mode, similar to subroutine:
  SWI CODE_1
Sets PC to 0x08.
Argument to SWI is passed to supervisor mode code.
Saves CPSR in SPSR.

## Slide 41: Exception
Exception: internally detected error.
Exceptions are synchronous with instructions but unpredictable.
Build exception mechanism on top of interrupt mechanism.
Exceptions are usually prioritized and vectorized.

## Slide 42: Trap
Trap (software interrupt): an exception generated by an instruction.
  Call supervisor mode.
ARM uses SWI instruction for traps.
SHARC offers three levels of software interrupts.
  Called by setting bits in IRPTL register.

## Slide 43: Co-processor
Co-processor: added function unit that is called by instruction.
  Floating-point units are often structured as co-processors.
ARM allows up to 16 designer-selected co-processors.
  Floating-point co-processor uses units 1 and 2.