## Slide 1: System design techniques
Private branch exchange (PBX).
Ink-jet printer.
PDAs.
Set-top boxes.
Systems-on-silicon.

## Slide 2: Digital telephone switches
High-end switches are highly reliable:
  30 seconds downtime per year.
Companies, homes install private branch exchanges (PBXs):
  intercom features;
  management of long distance charges.

## Slide 3: Telephone switching systems
Establish telephone calls:
  within switch, find other phone line;
  outside switch, find route to other line.
Route voice samples between phones.
Measure call time for billing.
Provide maintenance access to switch.
Notes: Basic tasks of a PBX.

## Slide 4: Telephone terminology
Line: distinct telephone connection.
Line card: PBX/subscriber line interface.
Off-hook: active telephone.
On-hook: inactive telephone.
Trunk line: phone lines between switches.
POTS: plain old telephone service (analog, no fancy services).
Notes: Off-hook/on-hook is most confusing.

## Slide 5: Computer-controlled telephone switching
Voice data rates:
  8 bits sample ( or A law);
  125  s period (8 kHz).
Telephones are I/O devices.
Computer bus is switch.
CPU
memory
line
card
line
card
Notes: Use bus and memory to transfer call data between line cards.
Must read one value from and write one value to each pone in the call on every sample.

## Slide 6: Dialing
Dual-tone multi-frequency (DTMF): tones define row, column of key.
Must be held for 0.1 sec.
1
2
3
4
5
6
7
8
9
*
0
#
Notes: One tone per row/column.
Sensing DTMF is relatively expensive.
Can’t get a dial tone until a DTMF detector is available.

## Slide 7: Call states
On-hook
Rcv ringing
Call
Off-hook
Dial
tone
Dialing
Place
ringing
Receive call
Place call
Incoming
call
Take off-hook
Return on-hook
Take off-hook
Dial decoder ready
Number
complete
Other phone
off-hook
Line 1
Line 2
Notes: State machine for a call.
Includes both sides of the call.
When we walked through this scenario, we realized that we had forgotten the Call->On-hook transition.

## Slide 8: PBX model
Calls are parallel processes:
Call coordination, billing, etc.
Call 1
Call n
...
Notes: Calls should not interfere with each other---specify as parallel operations.
Some coordination is required for billing, etc.

## Slide 9: Tigerswitch system architecture
PC platform.
  Switch calls over ISA bus.
Line cards are custom devices.
Notes: Some commercial PBXs are built on PC platform.

## Slide 10: DTMF sensing
Software process on CPU.
  Uses lots of CPU time.
Analog filter bank on line cards.
  Expensive in volume.
DSP on separate card.
  Requires new design.
CPU
memory
line
card
line
card
DTMF card
Notes: DTMF detection was too expensive to run on the CPU.
We chose to put analog detectors on line cards to avoid designing a separate DTMF card.
If you were building commercial PBXs, manufacturing cost may be more important than design time and you may choose the DTMF card.

## Slide 11: Switching
Process-per-call is bad implementation.
  Context switch per call per 125 s.
Unroll calls into one loop.
  Each loop iteration is one call for one sample.
for (i=0; i<n_calls; i++) {
/* from 1 to 2 */
data = read(call[i].line1);
write(call[i].line2,data);
/* from 2 to 1 */
data = read(call[i].line2);
write(call[i].line1,data);
}
Notes: Collapse set of processes into a table + loop.
Can collapse in this case because data arrivals are very regular, computations are very uniform.

## Slide 12: HP DesignJet drafting plotter
Plots up to 36 inches wide at 300 DPI.
Combines a variety of tasks:
  host communication;
  graphics language interpretation;
  rasterization;
  device control.

## Slide 13: The plotting process
HP-GL/2
PostScript
rasterizer
raster memory
plotter
controller

## Slide 14: Design considerations
Memory utilization is important.
  36 inches X large X 300 DPI X n bits/pixel is a lot of memory.
  Requires clever algorithms to minimize raster memory requirements.
Requires real-time control.
Requires concurrency: read new data, rasterize, control print head.

## Slide 15: HP DesignJet hardware architecture
i960KA
adrs
latch
bus
if
1 MB
ROM
2 MB
DRAM
proc.
support
ASIC
||
if
RS-
422
pen
ctrl
ASIC
swath
RAM
servo
proc.
(8052)
EEPROM
DRAM
ctrl
front panel
stepper
motor
carriage
PC board
Notes: i960 busincludes upper-right corner.
Separate communication paths not connected to bus allow deadline-driven communication between other components.

## Slide 16: Early architectural decisions
Chose Intel 80960KA as main processor.
  Handled parsing, rasterization control, print engine control.
  Multiplexed bus reduced pin count.
  Could be upgraded to floating-point if necessary.
Used modular I/O to host system.
Did not use disk for local storage.

## Slide 17: System components
2 MB RAM (SIMM sockets for more).
Three ASICs:
  pen interface;
  processor support;
  carriage.
Servo processing performed by 8052 microcontroller.

## Slide 18: Rasterization
Plot is generated in swaths.
  Separate swath memory.
Pixels are generated in row order by main processor.
Pixels are fed to pens in column order.
Pen interface ASIC transforms row order to column order.

## Slide 19: Data flows
i960KA
adrs
latch
bus
if
1 MB
ROM
2 MB
DRAM
proc.
support
ASIC
||
if
RS-
422
pen
ctrl
ASIC
swath
RAM
servo
proc.
(8052)
EEPROM
DRAM
ctrl
front panel
stepper
motor
carriage
PC board
parsing and rasterization
swath generation
drawing

## Slide 20: Operations
Servo processor controls stepper motor.
Carriage processor must write, read pen alignment marks.
Processor support ASIC provides multiple functions: interrupt and mailbox communication.
Motion controller decodes position of print carriage and paper; watchdogs servo.

## Slide 21: Pen interface ASIC
Interfaces to i960 bus, swath memory, carriage ASIC.
Pen interface reads pixels from swath in predetermined pattern using pixel address generator.
Must support bidirectional printing since head prints both ways.

## Slide 22: Carriage ASIC
Interrfaces to carriage processor bus, pen interface ASIC, servo controller.
Reads timing control registers using the CPU bus.
Delay registers add correction for pen alignment.

## Slide 23: Development process
Pixel shuffling algorithm for pen interface/carriage ASICs was prototyped in C.
Built emulators for ASICs to allow parallel development of i960 software and hardware.

## Slide 24: Software development environment
Plotter software could be run on Unix workstation or target platform.
  Differed in I/O and print engine subsystems.
  Print engine was emulated on host with X window interface showing swath state.
Used in-house RTOS.
HP-GL/2 parser was legacy code.

## Slide 25: Software development environment, cont’d.
Rewrote vector/raster converter from assembly language to C to port to i960.
Used gdb960 as monitor debugger on target system, communicating with host.
Front panel developed on PC, tested by user interface designers, marketing.
Paper loading designed by mechanical engineers.

## Slide 26: Personal digital assistant
PDA: portable, specialized information device.
Characteristics:
  low cost for consumer market;
  physically small;
  battery-powered;
  software-rich.

## Slide 27: Apple Newton
First modern PDA.
Original used ARM 610; later version used StrongARM.
Support operations in Runt ASIC: DMA, real-time clock, video interface, audio, PCMCIA.
Software written in NewtonScript language.

## Slide 28: Newton hardware architecture
ARM 610
ROM
RAM
Runt
ASIC
LCD
speaker
serial I/F
A/D
tablet
PCMCIA
infrared
Notes: Architecture reminiscent of PC: CPU, support chip, I/O devices.

## Slide 29: Motorola Envoy hardware architecture
PCMCIA
1 MB DRAM
4 MB flash
Astro
system
ASIC
68439
CPU
audio
modem
infrared
power supply
A/D
touchscreen
Magicbus
Notes: Architecture also reminiscen t of PC.
Note that memory is not directly connected to CPU.

## Slide 30: Feature creep
Designers tend to add features to system during design.
  Increases power consuption.
  Changes mechanical design.
  Makes software design more complex.
Software thrashing can reduce battery life.
Notes: Feature creep related to second-system syndrome (Brooks).

## Slide 31: PDA power supply
System must be designed to gracefully handle low battery power.
  Abrupt power loss can destroy lots of data in RAM.
Smart Battery System puts electronics in battery to measure battery performance.

## Slide 32: InfoPad
Brodersen et al: advanced networked multimedia information appliance.
System performed many functions on remote systems to increase battery life.
Made use of specialized hardware units to reduce power consumption over software implementation.

## Slide 33: InfoPad hardware architecture
Wireless network
interface
Speech
codec
Video
decompressor
ARM 60
display
Keyboard/pointer
other I/O
Notes: Used special-purpose hardware for speech, video.
Hardware less reminiscent of PC platform than were Newton, Envoy.

## Slide 34: Set-top boxes
Interface between cable/satellite and TV:
  digital television;
  user interface;
  may include back channel for purchases, etc.
Very cost-sensitive market.

## Slide 35: Set-top box in system
set-top box
IR
digital TV input
back
channel

## Slide 36: Philips fiber-to-curb box hardware
Network
interface
MPEG
demux
MPEG
audio
MPEG
video
NTSC
CD-I
graphics
PCMCIA
DRAM
I/O
kbd
IR
card
NVRAM
DRAM
DRAM
Notes: Architecture not so reminiscent of PC as were PDAs.
Use special-purpose hardware for MPEG decoding.
CD-I graphics renders on-screen user interface.

## Slide 37: Fiber-to-curb box software
default apps
custom apps
OS-9 kernel
I/O manager
device drivers
boot/monitor software
MPEG2
demux
audio/video
interfaces
CD-I
graphics
network
interface
processor
hardware
layer
OS
layer
application
layer

## Slide 38: Systems-on-silicon
Can build significant embedded systems on single chip:
  one or more high-performance CPUs;
  I/O devices;
  memory.
Advantages:
  higher performance and lower power;
  lower cost.

## Slide 39: Moore’s Law (Sematech)
108
109
2000
2012
PC on chip
billion-transistor
system-on-chip
Notes: We will be able to build 1 billion transistor chips in large volumes fairly soon.
We can already put enough transistors on a single chip to build a complete low-end PC, including main memory, CPU, etc.

## Slide 40: Design challenges
Core-based design: can’t take time to design gates, lines of code.
Custom architectures:
  heterogeneous multiprocessors;
  custom memory systems.
Verification:
  long turnaround time;
  can’t probe interior directly.
Notes: Must have huge designer productivity to build billion-transistor systems.
We will need customized architectures.
We will need new verification strategies.