## Slide 1: Processes and operating systems
Operating systems.

## Slide 2: Operating systems
The operating system controls resources:
  who gets the CPU;
  when I/O takes place;
  how much memory is allocated.
The most important resource is the CPU itself.
  CPU access controlled by the scheduler.

## Slide 3: Process state
A process can be in one of three states:
  executing on the CPU;
  ready to run;
  waiting for data.
executing
ready
waiting
gets data
and CPU
needs
data
gets data
needs data
preempted
gets
CPU

## Slide 4: Operating system structure
OS needs to keep track of:
  process priorities;
  scheduling state;
  process activation record.
Processes may be created:
  statically before system starts;
  dynamically during execution.

## Slide 5: Embedded vs. general-purpose scheduling
Workstations try to avoid starving processes of CPU access.
  Fairness = access to CPU.
Embedded systems must meet deadlines.
  Low-priority processes may not run for a long time.

## Slide 6: Priority-driven scheduling
Each process has a priority.
CPU goes to highest-priority process that is ready.
Priorities determine scheduling policy:
  fixed priority;
  time-varying priorities.

## Slide 7: Priority-driven scheduling example
Rules:
  each process has a fixed priority (1 highest);
  highest-priority ready process gets CPU;
  process continues until done or wait state.
Processes
  P1: priority 1, execution time 10
  P2: priority 2, execution time 30
  P3: priority 3, execution time 20

## Slide 8: Priority-driven scheduling example
time
P2 ready t=0
P1 ready t=15
P3 ready t=18
0
30
10
20
60
40
50
P2
P2
P1
P3

## Slide 9: The scheduling problem
Can we meet all deadlines?
  Must be able to meet deadlines in all cases.
How much CPU horsepower do we need to meet our deadlines?

## Slide 10: Process initiation disciplines
Periodic process: executes on (almost) every period.
Aperiodic process: executes on demand.
Analyzing aperiodic process sets is harder---must consider worst-case combinations of process activations.

## Slide 11: Timing requirements on processes
Period: interval between process activations.
Initiation interval: reciprocal of period.
Initiation time: time at which process becomes ready.
Deadline: time at which process must finish.

## Slide 12: Timing violations
What happens if a process doesn’t finish by its deadline?
  Hard deadline: system fails if missed.
  Soft deadline: user may notice, but system doesn’t necessarily fail.

## Slide 13: Example: Space Shuttle software error
Space Shuttle’s first launch was delayed by a software timing error:
  Primary control system PASS and backup system BFS.
  BFS failed to synchronize with PASS.
  Change to one routine added delay that threw off start time calculation.
  1 in 67 chance of timing problem.

## Slide 14: Interprocess communication
Interprocess communication (IPC): OS provides mechanisms so that processes can pass data.
Two types of semantics:
  blocking: sending process waits for response;
  non-blocking: sending process continues.

## Slide 15: IPC styles
Shared memory:
  processes have some memory in common;
  must cooperate to avoid destroying/missing messages.
Message passing:
  processes send messages along a communication channel---no common address space.

## Slide 16: Shared memory
Shared memory on a bus:
CPU 1
CPU 2
memory

## Slide 17: Race condition in shared memory
Problem when two CPUs try to write the same location:
  CPU 1 reads flag and sees 0.
  CPU 2 reads flag and sees 0.
  CPU 1 sets flag to one and writes location.
  CPU 2 sets flag to one and overwrites location.

## Slide 18: Atomic test-and-set
Problem can be solved with an atomic test-and-set:
  single bus operation reads memory location, tests it, writes it.
ARM test-and-set provided by SWP:
    ADR r0,SEMAPHORE
    LDR r1,#1
    GETFLAG SWP r1,r1,[r0]
    BNZ GETFLAG

## Slide 19: Critical regions
Critical region: section of code that cannot be interrupted by another process.
Examples:
  writing shared memory;
  accessing I/O device.

## Slide 20: Semaphores
Semaphore: OS primitive for controlling access to critical regions.
Protocol:
  Get access to semaphore with P().
  Perform critical region operations.
  Release semaphore with V().

## Slide 21: Message passing
Message passing on a network:
CPU 1
CPU 2
message
message
message

## Slide 22: Process data dependencies
One process may not be able to start until another finishes.
Data dependencies defined in a task graph.
All processes in one task run at the same rate.
P1
P2
P3
P4

## Slide 23: Other operating system functions
Date/time.
File system.
Networking.
Security.