## Slide 1: Program design and analysis
Design patterns
Representations of programs
Assembly and linking

## Slide 2: Design patterns
Design pattern: generalized description of the design of a certain type of program.
Designer fills in details to customize the pattern to a particular programming problem.

## Slide 3: List design pattern
List
create()
add-element()
delete-element()
find-element()
destroy()
List-element
1
*

## Slide 4: Design pattern elements
Class diagram
State diagrams
Sequence diagrams
etc.

## Slide 5: State machine
State machine is useful in many contexts:
  parsing user input
  responding to complex stimuli
  controlling sequential outputs

## Slide 6: State machine example
idle
buzzer
seated
belted
no seat/-
seat/timer on
no belt
and no
timer/-
no belt/timer on
belt/-
belt/
buzzer off
Belt/buzzer on
no seat/-
no seat/
buzzer off

## Slide 7: State machine pattern
State machine
state
output step(input)

## Slide 8: C implementation
#define IDLE 0
#define SEATED 1
#define BELTED 2
#define BUZZER 3
switch (state) {
case IDLE: if (seat) { state = SEATED; timer_on = TRUE; }
break;
case SEATED: if (belt) state = BELTED;
else if (timer) state = BUZZER;
break;
…
}

## Slide 9: Circular buffer
x1
x2
x3
x4
x5
x6
t1
t2
t3
Data stream
x1
x2
x3
x4
Circular buffer
x5
x6
x7

## Slide 10: Circular buffer pattern
Circular buffer
init()
add(data)
data head()
data element(index)

## Slide 11: Circular buffer implementation: FIR filter
int circ_buffer[N], circ_buffer_head = 0;
int c[N]; /* coefficients */
…
int ibuf, ic;
for (f=0, ibuff=circ_buff_head, ic=0;
ic<N; ibuff=(ibuff==N-1?0:ibuff++), ic++)
f = f + c[ic]*circ_buffer[ibuf];

## Slide 12: Models of programs
Source code is not a good representation for programs:
  clumsy;
  leaves much information implicit.
Compilers derive intermediate representations to manipulate and optiize the program.

## Slide 13: Data flow graph
DFG: data flow graph.
Does not represent control.
Models basic block: code with no entry or exit.
Describes the minimal ordering requirements on operations.

## Slide 14: Single assignment form
x = a + b;
y = c - d;
z = x * y;
y = b + d;
original basic block
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
single assignment form

## Slide 15: Data flow graph
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
single assignment form
+
-
+
*
DFG
a
b
c
d
z
x
y
y1

## Slide 16: DFGs and partial orders
Partial order:
a+b, c-d; b+d x*y
Can do pairs of operations in any order.
+
-
+
*
a
b
c
d
z
x
y
y1

## Slide 17: Control-data flow graph
CDFG: represents control and data.
Uses data flow graphs as components.
Two types of nodes:
  decision;
  data flow.

## Slide 18: Data flow node
Encapsulates a data flow graph:
Write operations in basic block form for simplicity.
x = a + b;
y = c + d

## Slide 19: Control
cond
T
F
Equivalent forms
value
v1
v2
v3
v4

## Slide 20: CDFG example
if (cond1) bb1();
else bb2();
bb3();
switch (test1) {
case c1: bb4(); break;
case c2: bb5(); break;
case c3: bb6(); break;
}
cond1
bb1()
bb2()
bb3()
bb4()
test1
bb5()
bb6()
T
F
c1
c2
c3

## Slide 21: for loop
for (i=0; i<N; i++)
loop_body();
for loop
i=0;
while (i<N) {
loop_body(); i++; }
equivalent
i<N
loop_body()
T
F
i=0

## Slide 22: Assembly and linking
Last steps in compilation:
HLL
compile
assembly
assemble
HLL
HLL
assembly
assembly
link
executable
link

## Slide 23: Multiple-module programs
Programs may be composed from several files.
Addresses become more specific during processing:
  relative addresses are measured relative to the start of a module;
  absolute addresses are measured relative to the start of the CPU address space.

## Slide 24: Assemblers
Major tasks:
  generate binary for symbolic instructions;
  translate labels into addresses;
  handle pseudo-ops (data, etc.).
Generally one-to-one translation.
Assembly labels:
  ORG 100
  label1 ADR r4,c

## Slide 25: Symbol table
ADD r0,r1,r2
xx ADD r3,r4,r5
CMP r0,r3
yy SUB r5,r6,r7
assembly code
xx 0x8
yy 0x10
symbol table

## Slide 26: Symbol table generation
Use program location counter (PLC) to determine address of each location.
Scan program, keeping count of PLC.
Addresses are generated at assembly time, not execution time.

## Slide 27: Symbol table example
ADD r0,r1,r2
xx ADD r3,r4,r5
CMP r0,r3
yy SUB r5,r6,r7
xx 0x8
yy 0x10
PLC=0x7
PLC=0x7
PLC=0x7
PLC=0x7

## Slide 28: Two-pass assembly
Pass 1:
  generate symbol table
Pass 2:
  generate binary instructions

## Slide 29: Relative address generation
Some label values may not be known at assembly time.
Labels within the module may be kept in relative form.
Must keep track of external labels---can’t generate full binary for instructions that use external labels.

## Slide 30: Pseudo-operations
Pseudo-ops do not generate instructions:
  ORG sets program location.
  EQU generates symbol table entry without advancing PLC.
  Data statements define data blocks.

## Slide 31: Linking
Combines several object modules into a single executable module.
Jobs:
  put modules in order;
  resolve labels across modules.

## Slide 32: Externals and entry points
external reference
entry point
xxx ADD r1,r2,r3
B a
yyy %1
a ADR r4,yyy
ADD r3,r4,r5

## Slide 33: Module ordering
Code modules must be placed in absolute positions in the memory space.
Load map or linker flags control the order of modules.
module1
module2
module3

## Slide 34: Dynamic linking
Some operating systems link modules dynamically at run time:
  shares one copy of library among all executing programs;
  allows programs to be updated with new versions of libraries.