## Slide 1: SHARC instruction set
SHARC programming model.
SHARC assembly language.
SHARC memory organization.
SHARC data operations.
SHARC flow of control.

## Slide 2: SHARC programming model
Register files:
  R0-R15 (aliased as F0-F15 for floating point)
Status registers.
Loop registers.
Data address generator registers.
Interrupt registers.

## Slide 3: SHARC assembly language
Algebraic notation terminated by semicolon:
  R1=DM(M0,I0), R2=PM(M8,I8); ! comment
  label: R3=R1+R2;
data memory access
program memory access

## Slide 4: SHARC memory space
IOP registers
0x0
256
forbidden
normal word
addressing
short word
addressing
0x20000
0x40000
interrupt vectors

## Slide 5: SHARC data types
32-bit IEEE single-precision floating-point.
40-bit IEEE extended-precision floating-point.
32-bit integers.
Memory organized internally as 32-bit words.

## Slide 6: SHARC microarchitecture
Modified Harvard architecture.
  Program memory can be used to store some data.
Register file connects to:
  multiplier
  shifter;
  ALU.

## Slide 7: SHARC mode registers
Most important:
  ASTAT: arithmetic status.
  STKY: sticky.
  MODE 1: mode 1.

## Slide 8: Rounding and saturation
Floating-point can be:
  rounded toward zero;
  rounded toward nearest.
ALU supports saturation arithmetic (ALUSAT bit in MODE1).
  Overflow results in max value, not rollover.

## Slide 9: Multiplier
Fixed-point operations can accumulate into local MR registers or be written to register file. Fixed-point result is 80 bits.
Floating-point results always go to register file.
Status bits: negative, under/overflow, invalid, fixed-point undeflow, floating-point unerflow, floating-point invalid.

## Slide 10: ALU/shifter status flags
ALU:
  zero, overflow, negative, fixed-point carry, inputsign, floating-point invalid, last op was floating-point, compare accumulation registers, floating-point under/oveflow, fixed-point overflow, floating-point invalid
Shifter:
  zero, overflow, sign

## Slide 11: Flag operations
All ALU operations set AZ (zero), AN (negative), AV (overflow), AC (fixed-point carry), AI (floating-point invalid) bits in ASTAT.
STKY is sticky version of some ASTAT bits.

## Slide 12: Example: data operations
Fixed-point -1 + 1 = 0:
  AZ = 1, AU = 0, AN = 0, AV = 0, AC = 1, AI = 0.
  STKY bit AOS (fixed point underflow) not set.
Fixed-point -2*3:
  MN = 1, MV = 0, MU = 1, MI = 0.
  Four STKY bits, none of them set.
LSHIFT 0x7fffffff BY 3: SZ=0,SV=1,SS=0.

## Slide 13: Multifunction computations
Can issue some computations in parallel:
  dual add-subtract;
  fixed-point multiply/accumulate and add,subtract,avaeage
  floating-point multiply and ALU operatoin
  multiplication and dual add/subtract
Multiplier operand from R0-R7, ALU operand from R8-R15.

## Slide 14: SHARC load/store
Load/store architecture: no memory-direct operations.
Two data address generators (DAGs):
  program memory;
  data memory.
Must set up DAG registers to control loads/stores.

## Slide 15: DAG1 registers
I0
I1
I2
I3
I4
I5
I6
I7
M0
M1
M2
M3
M4
M5
M6
M7
L0
L1
L2
L3
L4
L5
L6
L7
B0
B1
B2
B3
B4
B5
B6
B7

## Slide 16: Data address generators
Provide indexed, modulo, bit-reverse indexing.
MODE1 bits determine whether primary or alternate registers are active.

## Slide 17: BASIC addressing
Immediate value:
  R0 = DM(0x20000000);
Direct load:
  R0 = DM(_a); ! Loads contents of _a
Direct store:
  DM(_a)= R0; ! Stores R0 at _a

## Slide 18: Post-modify with update
I register holds base address.
M register/immediate holds modifier value.
R0 = DM(I3,M3) ! Store
DM(I2,1) = R1 ! Load
Circular buffer: L register is buffer start index, B is buffer base address.

## Slide 19: Data in program memory
Can put data in program memory to read two values per cycle:
F0 = DM(M0,I0), F1 = PM(M8,I9);
Compiler allows programmer to control which memory values are stored in.

## Slide 20: Example: C assignments
C:
  x = (a + b) - c;
Assembler:
  R0 = DM(_a) ! Load a
  R1 = DM(_b); ! Load b
  R3 = R0 + R1;
  R2 = DM(_c); ! Load c
  R3 = R3-R2;
  DM(_x) = R3; ! Store result in x

## Slide 21: Example, cont’d.
C:
  y = a*(b+c);
Assembler:
  R1 = DM(_b) ! Load b
  R2 = DM(_c); ! Load c
  R2 = R1 + R2;
  R0 = DM(_a); ! Load a
  R2 = R2-R0;
  DM(_y) = R23; ! Store result in yx

## Slide 22: Example, cont’d.
Shorter version using pointers:
! Load b, c
R2=DM(I1,M5), R1=PM(I8,M13);
R0 = R2+R1, R12=DM(I0,M5);
R6 = R12*R0(SSI);
DM(I0,M5)=R8; ! Store in y

## Slide 23: Example, cont’d.
C:
  z = (a << 2) | (b & 15);
Assembler:
R0=DM(_a); ! Load a
R0=LSHIFT R0 by #2; ! Left shift
R1=DM(_b); R3=#15; ! Load immediate
R1=R1 AND R3;
R0 = R1 OR R0;
DM(_z) = R0;

## Slide 24: SHARC program sequencer
Features:
  instruction cache;
  PC stack;
  status registers;
  loop logic;
  data addres generator;

## Slide 25: Conditional instructions
Instructions may be executed conditionally.
Conditions come from:
  arithmetic status (ASTAT);
  mode control 1 (MODE1);
  flag inputs;
  loop counter.

## Slide 26: SHARC jump
Unconditional flow of control change:
  JUMP foo
Three addressing modes:
  direct;
  indirect;
  PC-relative.

## Slide 27: Branches
Types: CALL, JUMP, RTS, RTI.
Can be conditional.
Address can be direct, indirect, PC-relative.
Can be delayed or non-delayed.
JUMP causes automatic loop abort.

## Slide 28: Example: C if statement
C:
  if (a > b) { x = 5; y = c + d; } else x = c - d;
Assembler:
! Test
R0 = DM(_a); R1 = DM(_b);
COMP(R0,R1); ! Compare
IF GE JUMP fblock;

## Slide 29: C if statement, cont’d.
! True block
tblock: R0 = 5; ! Get value for x
DM(_x) = R0;
R0 = DM(_c); R1 = DM(_d);
R1 = R0+R1;
DM(_y)=R1;
JUMP other; ! Skip false block

## Slide 30: C if statement, cont’d.
! False block
fblock: R0 = DM(_c);
R1 = DM(_d);
R1 = R0-R1;
DM(_x) = R1;
other: ! Code after if

## Slide 31: Fancy if implementation
C:
if (a>b) y = c-d; else y = c+d;
Use paralleism to speed it up---compute both cases, then choose which one to store.

## Slide 32: Fancy if implementation, cont’d.
! Load values
R1=DM(_a); R2=DM(_b);
R3=DM(_c); R4=DM(_d);
! Compute both sum and difference
R12 = r2+r4, r0 = r2-r4;
! Choose which one to save
comp(r8,r1);
if ge r0=r12;
dm(_y) = r0 ! Write to y

## Slide 33: DO UNTIL loops
DO UNTIL instruction provides efficient looping:
LCNTR=30, DO label UNTIL LCE;
R0=DM(I0,M0), F2=PM(I8,M8)
R1=R0-R15;
label: F4=F2+F3;
Loop length
Last instruction in loop
Termination
condition

## Slide 34: Example: FIR filter
C:
  for (i=0, f=0; i<N; i++)
  f = f + c[i]*x[i];

## Slide 35: FIR filter assembler
! setup
I0=_a; I8=b; ! a[0] (DAG0), b[0] (DAG1)
M0=1; M8=1 ! Set up increments
! Loop body
LCNTR=N, DO loopend UNTIL LCE;
! Use postincrement mode
R1=DM(I0,M0), R2=PM(I8,M8);
loopend: R8=R1*R2, R12=R12+R9;

## Slide 36: Optimized FIR filter code
I4=_a; I12=_b;
R4 = R4 xor R4, R1=DM(I4,M6), R2=PM(I12,M14);
MR0F = R4, MODIFY(I7,M7);
! Start loop
LCNTR=20, DO(PC,loop) UNTIL LCE;
loop: MRF=MRF+42*R1 (SSI), R1=DM(I4,M6), R2=PM(I12,M14);
! Loop cleanup
R0=MR0F;

## Slide 37: SHARC subroutine calls
Use CALL instruction:
  CALL foo;
Can use absolute, indirect, PC-relative addressing modes.
Return using RTS instruction.

## Slide 38: PC stack
PC stack: 30 locations X 24 instructions.
Return addresses for subroutines, interrupt service routines, loops held in PC stack.

## Slide 39: Example: C function
C:
  void f1(int a) { f2(a); }
Assembler:
f1: R0=DM(I1,-1); ! Load arg into R0
DM(I1,M1)=R0; ! Push f2’s arg
CALL f2;
MODIFY(I1,-1); ! Pop element
RTS;

## Slide 40: Important programming reminders
Non-delayed branches (JUMP, CALL, RTS, RTI) do not execute 2 following instructions. Delayed branches are available.
Cache miss costs at least one cycle to allow program memory bus to complete.

## Slide 41: Important programming reminders, cont’d
Extra cache misses in loops:
  misses on first and last loop iteration if data memory is accessed in last 2 instructions of loop;
  3 misses if loop has only one instruction which requires a program memory bus access.
1-instr. loops should be executed 3 times, 2-instr. loops 2 times to avoid NOPs.

## Slide 42: Important programming reminders, cont’d
NOPs added for DAG register write followed by DAG data addressing in same register bank.
Can program fixed wait states or ACK.
Interrupt does not occur until 2 instructions after delayed branch.
Initialize circular buffer by setting L to positive value, loading B to base.

## Slide 43: Important programming reminders, cont’d
Some DAG register transfers are disallowed.
When given 2 writes to same register file in same cycle, only one actually occurs.
Fixed- to floating-point conversion always rounds to 40 bits.
Only DM bus can access all memory spaces.

## Slide 44: Important programming reminders, cont’d
When mixing 32-bit and 48-bit words in a block, all instructions must be below data.
16-bit short words are extended to 32 bits.
For dual data access, use DM for data-only access, PM for mixed data/instruction block. Instruction comes from cache.
A variety of conditions cause stalls.