## Slide 1: Compact disc players
Device characteristics.
Hardware architectures.
Software.

## Slide 2: CD audio
44.1 kHz sample rate.
16 bit samples.
Stereo.
Additional data tracks.

## Slide 3: Compact disc
Data stored on bottom of disc:
substrate
aluminum
coating
plastic
coating

## Slide 4: CD medium
Rotational speed: 1.2-1.4 m/s (CLV).
Track pitch: 1.6 microns.
Diameter: 120 mm.
Pit length: 0.8 -3 microns.
Pit depth: .11 microns.
Pit width: 0.5 microns.
Laser wavelength: 780 nm.

## Slide 5: CD layout
Data stored in spiral, not concentric circle:

## Slide 6: CD mechanism
Laser, lens:
laser
CD
detectors
diffraction
grating

## Slide 7: Laser focus
Focus controlled by vertical position of lens.
Unfocused beam causes irregular spot:
In focus
Out of focus
Out of focus

## Slide 8: Laser pickup
A
B
C
D
F
E
Side spot
detectors
Level:
A+B+C+D
Focus error:
(A+C)-(B+D)
Tracking error:
E-F

## Slide 9: Servo control
Four main signals:
  focus (laser) @ 245 kHz;
  tracking (laser) @ 245 kHz;
  sled (motor): @ 800 Hz;
  Disc motor.
Optical pickup

## Slide 10: EFM
Eight-to-fourteen modulation:
  Fourteen-bit code guarantees a maximum distance between transitions.
00000011
00100100000000

## Slide 11: Error correction
CD capacity: 6.99 GB raw, 700 MB formatted.
Reed-Solomon code:
  g(x) = (x-) (x- 2) … (x- n-k-1) (x- n-k)
Produces data, erasure bits.
Time to solve varies greatly depending on noise.
CD interleaves Reed-Solomon blocks to reduce effects of large data gaps.

## Slide 12: CIRC encoding
Cross-interleaved Reed-Solomon coding.
  Interleaves to reduce burst errors.
Each 16-bit sample split into two 8-bit symbols.
Specs:
  Max correctable burst: 4000 bits = 2.5 mm
  Max interpolatable burst: 12,300 bits = 7.7 bits

## Slide 13: CIRC algorithm
Sample split into two symbols.
Six samples from each sample (=24 symbols) are chosen.
Samples are delayed and scrambled.
Parity symbols (Q symbols) are generated.
Values are delayed by various amounts.
P parity symbols are generated.
Even words delayed by one symbol, P and Q words are inverted.
Frame = 32 8-bit symbols.

## Slide 14: Control word
8-bit control word for every 32-symbol block:
  P: 1 during music/lead-in, 0 at start of selection.
  Q: track number, time, etc (spread over 98 bits).
  R, S, T, U, V, W: reserved.

## Slide 15: Control and error correction
Skips caused by physical disturbance.
  Wait for disturbance to subside.
  Retry.
Read errors caused by disc/servo problems.
  Detect error.
  Choose location for retry.
  Retry.
  Fail and interpolate.

## Slide 16: Retry problems
Data is stored in a spiral.
  Can’t seek track as on magnetic disc.
  Sled servo is very coarse.
Data is only weakly addressed.
  Must read data to know where to go.

## Slide 17: Audio playback
Audio CD needs no audio processing.
Tasks:
  convert to analog;
  amplify.

## Slide 18: Digital/analog conversion
1-bit MASH conversion:
interpolation
noise
shaping
PWM
integrator

## Slide 19: MP3
Decoding is easier than encoding, but requires:
  decompression;
  filtering.
Basic CD standard for data discs.
No standards for MP3 disc file structure: player must understand Windows, Mac, Unix discs.

## Slide 20: Jog/skip memory
Read samples into RAM, play back from RAM.
Modern RAMs are larger than needed for reasonable jog/skip.
Jog memory saves some power.

## Slide 21: DVD format
Similar to CD, but:
  shorter wavelength laser;
  tighter pits;
  two layers of data.

## Slide 22: CD/MP3 player
Audio
CPU
amp
Jog
memory
Error
corrector
Servo
CPU
Analog
in
Analog
out
FE, TE, amp
focus,
tracking,
sled,
motor
head
drive
memory
memory
display
DAC
I2S

## Slide 23: Audio on DVD
Alternatives:
  MP3 on data DVD (stereo).
  Audio track of video DVD (5.1).
  DVD audio (5.1).
  SACD (5.1).